## Slide 1
Digital Signal Processing
Project Presentation
EECE – 312
Section – A
Group – 03

## Slide 2
Naimujjaman
Lamiya Mahbub
Mehrab Ibne Masud Badhon
Juthika Alamgir Orpa
Muntasir Ahmed
Gourab Datta
Group Members

## Slide 3
Digital Hearing Aid Compensating for Hearing Loss of Different Level

## Slide 4
Mild Hearing Loss
Normal Hearing
27dB-40dB
40dB-70dB
70dB – 90dB
>90dB
-10dB -26dB
05
04
03
02
01
Moderate Hearing Loss
Severe hearing loss
Profound Hearing loss
Classification of Hearing Loss and Hearing Level

## Slide 5
01
02
03
Amplifier increases
the strength of the
digital signal
The speaker produces
the amplified sound
into the ear
Microphone receives
sound and converts it
into a digital signal
Working Principle

## Slide 6
Band Pass Filter

## Slide 7
Procedure
03
02
05
04
01
Noise Reduction Filter
Noise Addition (AWGN)
Amplification According to Preference
Desired Signal
Input Signal

## Slide 8
Declare a function called 'hearing aid'
Insert A built in matlab audio named " HANDEL'
Add Awgn Noise with SNR=40 as a pretention of background noise
Denoise the signal using a low pass filter by designing using fixed parameters
denoised signal is inseted into a frequency shaper
design a Band pass filter
insert the cut off frequency of the band pass filter according to loss level
denoised signal filtered by bandpass and amplified
the filtered sound is converted to frequency domain using FFT
Spectrogram is analysed which takes into account of Amplitude, frequency and time domain
phase values are saved
magnitude shaping using threshold=1000
when amplitude shaped, saved phases are multiplied
IFFT is done on the amplitude shaped version
A time domain signal according to preference is played
spectogram of noised signal and final signal is obtained in GUI
Algorithm

## Slide 9
function hearing_aid(app,Fst1,Fp1,Fp2,Fst2,Ast1,Ap,Ast2) %code declared as function
app.StateEditField.Value=('input sound’) %shows in state when input
sound is playing
load handel.mat
fs=Fs; %imprting data got from handel.mat
y = y(:, 1); %for 1 sec
plot(app.UIAxes,y); %uiaxes shows the graph in matlab gui
app.StateEditField.Value=('playing actual sound...')
sound(y);
pause(10)
Inserting Sample Audio

## Slide 10
Input Signal Curve

## Slide 11
y = awgn(y,40);
noi = y;
plot(app.UIAxes2,y);
app.StateEditField.Value=('playing added noise...’); %shows in state
bar in gui
sound(y); %playing the sound
pause(10) %pausing the sound in 10 sec
Adding Noise to the Audio

## Slide 12
Sample Audio with Noise Curve

## Slide 13
hlpf = fdesign.lowpass('Fp,Fst,Ap,Ast',3.0e3,3.5e3,0.5,50,fs); %designing
lowpass filter using builtin function
[ Fp= passband frequency
Fst= stopband frequency
Ap=passband ripple
Ast = stopband ripple ]
D = design(hlpf); %lowpass filter
%freqz(D); %needed if we want the spectrum of the filter
x = filter(D,y); %filtering the noised signal
app.StateEditField.Value=('playing denoised sound’); %showed in state while
playing the sound
plot(app.UIAxes3,x); %plotting in the 3rd graph in gui
sound(x,fs); %playing the denoised sound
pause(10) %pause after 10 sec
Denoising Process Using a Low Pass Filter

## Slide 14
Denoised Audio Curve

## Slide 15
T = 1/fs; %setting time
len = length(x);
p = log2(len); %level division denoised signal
p = ceil(p); %making p an integer
N = 2^p; %number of level
f1 = fdesign.bandpass(Fst1,Fp1,Fp2,Fst2,Ast1,Ap,Ast2,5*fs);%setting
the values according to the requirement
hd = design(f1,'equiripple’); %bandpass function
y = filter(hd,x); %denoised signal filtered by bandpass
%freqz(hd); %filter frequency response if needed
y = y*100; %amplification
app.StateEditField.Value=('playing frequency shaped...');
sound(y,fs); %playing the freq shaped sound
pause(10); %pause after 10 sec
Frequency Shaping Using Band Pass of
Denoised Signal

## Slide 16
app.StateEditField.Value=('amplitude shaper')
out1=fft(y);
phse=angle(out1);%saving the phase values before amp shaping
mag=abs(out1)/N;%magnitude of freq shaped signal
[magsig,~]=size(mag);
threshold=1000;
out=zeros(magsig,1);
for i=1:magsig/2
if(mag(i)>threshold)
mag(i)=threshold;mag(magsig-i)=threshold;
end
out(i)=mag(i)*exp(j*phse(i));%setting the magnitudes same as
the previous position by multiplying exp phase
out(magsig-i)=out(i);
end
Amplitude Shaping of Frequency Shaped Signal
Using Threshold

## Slide 17
outfinal=real(ifft(out))*10000; %taking only real value after ifft of the
amp shaped signal
app.StateEditField.Value=('playing amplitude shaped...');
sound(outfinal,fs); %playing the finally edited sound
pause(10);%pause after 10 sec
Final Output in Time Domain Using IFFT

## Slide 18
myAxe = app.UIAxes4;
[S,F,T] = spectrogram(noi);
imagesc(myAxe, F, T, log(abs(S))); %plot the log spectrum as image
(noise added signal)
myAxe1 = app.UIAxes5;
[S1,F1,T1] = spectrogram(outfinal);
imagesc(myAxe1, F1, T1, log(abs(S1))); %plot the log spectrum as image ( final signal )
app.StateEditField.Value=('Thank you');
end
end
Finding the Spectrum of Noisy and
Adjusted Signal

## Slide 19
Spectrogram of Noisy Signal and Adjusted Signal

## Slide 20
Different Scenarios
mild
Required Gain: 27-40 DB
Starting Passband Frequency = 2000 Hz
Ending passband frequency = 5000 Hz
Patient No.1
severe
Required Gain: 70-90 DB
Starting Passband Frequency = 500 Hz
Ending passband frequency = 12000 Hz
moderate
Required Gain: 40-70 DB
Starting Passband Frequency = 3000 Hz
Ending passband frequency = 6000 Hz
Patient No.2
Patient No.3
Patient No.4

## Slide 21
Patient No. 1: Mild Hearing Loss

## Slide 22
Patient No. 2: Moderate Hearing Loss

## Slide 23
Patient No. 3: Severe Hearing Loss

## Slide 24
Patient No. 4: Profound Hearing Loss

## Slide 25
01
Can be connected to other devices
02
Decrease the risk of further
Hearing loss
03
Restores sound perception
to natural levels.
APPLICATIONS

## Slide 26
Applying machine learning or deep learning the accuracy can me improved much further
Algorithm can be further improved in the threshold region to decrease or
increase the level of hearing.
Dynamic SQNR may be added to deal with crowded place
User level sound volume input
Scope for Improvement

## Slide 27
CONCLUSION
Implementation of Fast Fourier Transform gave
Special access to modifying the frequency and amplitude and opened up the gates for further dynamic adjustment and digitalization
signal is more suitable for hearing
impaired
people with less complexity
and more flexibility.
01
02

## Slide 28
ANY
QUESTIONS?

## Slide 29
X=‘Thank You’
DISP(X)